## Slide 1: CCNA Security
Chapter Five
Implementing Intrusion Prevention

## Slide 2: Lesson Planning
This lesson should take 3-6 hours to present
The lesson should include lecture, demonstrations, discussion and assessments
The lesson can be taught in person or using remote instruction

## Slide 3: Major Concepts
Describe the purpose and operation of network-based and host-based Intrusion Prevention Systems (IPS)
Describe how IDS and IPS signatures are used to detect malicious network traffic
Implement Cisco IOS IPS operations using CLI and SDM
Verify and monitor the Cisco IOS IPS operations using CLI and SDM

## Slide 4: Lesson Objectives
Upon completion of this lesson, the successful participant will be able to:
  Describe the functions and operations of IDS and IPS systems
  Introduce the two methods of implementing IPS and describe host based IPS
  Describe network-based intrusion prevention
  Describe the characteristics of IPS signatures
  Describe the role of signature alarms (triggers) in Cisco IPS solutions
  Describe the role of tuning signature alarms (triggers) in a Cisco IPS solution

## Slide 5: Lesson Objectives
Describe the role of signature actions in a Cisco IPS solution
Describe the role of signature monitoring in a Cisco IPS solution
Describe how to configure Cisco IOS IPS Using CLI
Describe how to configure Cisco IOS IPS using Cisco SDM
Describe how to modify IPS signatures in CLI and SDM
Describe how to verify the Cisco IOS IPS configuration
Describe how to monitor the Cisco IOS IPS events
Describe how to troubleshoot the Cisco IOS IPS events
Notes: 5

## Slide 6: Common Intrusions
MARS
Remote Worker
Remote Branch
VPN
VPN
VPN
ACS
Iron Port
Firewall
Web Server
Email Server
DNS
LAN
CSA
Zero-day exploit
attacking the network

## Slide 7: Intrusion Detection Systems (IDSs)
An attack is launched on a network that has a sensor deployed in promiscuous IDS mode; therefore copies of all packets are sent to the IDS sensor for packet analysis. However, the target machine will experience the malicious attack.
The IDS sensor, matches the malicious traffic to a signature and sends the switch a command to deny access to the source of the malicious traffic.
The IDS can also send an alarm to a management console for logging and other management purposes.
Switch
Management Console
1
2
3
Target
Sensor

## Slide 8: Intrusion Prevention Systems (IPSs)
An attack is launched on a network that has a sensor deployed in IPS mode (inline mode).
The IPS sensor analyzes the packets as they enter the IPS sensor interface. The IPS sensor matches the malicious traffic to a signature and the attack is stopped immediately.
The IPS sensor can also send an alarm to a management console for logging and other management purposes.
Traffic in violation of policy can be dropped by an IPS sensor.
Sensor
Management Console
1
2
3
Target
4
Bit Bucket

## Slide 9: Common characteristics of IDS and IPS
Both technologies are deployed using sensors.
Both technologies use signatures to detect patterns of misuse in network traffic.
Both can detect atomic patterns (single-packet) or composite patterns (multi-packet).

## Slide 10: Comparing IDS and IPS Solutions
 | Advantages | Disadvantages
 | No impact on network (latency, jitter) No network impact if there is a sensor failure No network impact if there is sensor overload | Response action cannot stop trigger packets Correct tuning required for response actions Must have a well thought-out security policy More vulnerable to network evasion techniques
IDS Promiscuous Mode

## Slide 11: Comparing IDS and IPS Solutions
 | Advantages | Disadvantages
 | Stops trigger packets Can use stream normalization techniques | Sensor issues might affect network traffic Sensor overloading impacts the network Must have a well thought-out security policy Some impact on network (latency, jitter)
IPS Inline Mode

## Slide 12: Network-Based Implementation
MARS
Remote Worker
Remote Branch
VPN
VPN
VPN
Iron Port
Firewall
Web Server
Email Server
DNS
IPS
CSA
CSA
CSA
CSA
CSA

## Slide 13: Host-Based Implementation
MARS
Remote Worker
Remote Branch
VPN
VPN
VPN
Iron Port
Firewall
IPS
CSA
CSA
Web Server
Email Server
DNS
CSA
CSA
CSA
CSA
CSA
CSA
CSA
Agent
Management Center for Cisco Security Agents

## Slide 14: Cisco Security Agent
Firewall
Corporate
Network
DNS
Server
Web
Server
Management Center for Cisco Security Agents
SMTP Server
Application
Server
Agent
Agent
Agent
Agent
Agent
Agent
Untrusted Network
Agent
Agent
Agent
video

## Slide 15: Cisco Security Agent Screens
A waving flag in the system tray indicates a potential security problem.
CSA maintains a log file allowing the user to verify problems and learn more information.
A warning message appears when CSA detects a Problem.

## Slide 16: Host-Based Solutions
Advantages | Disadvantages
The success or failure of an attack can be readily determined. HIPS does not have to worry about fragmentation attacks or variable Time to Live (TTL) attacks. HIPS has access to the traffic in unencrypted form. | HIPS does not provide a complete network picture. HIPS has a requirement to support multiple operating systems.
Advantages and Disadvantages of HIPS

## Slide 17: Network-Based Solutions
Management
Server
Corporate
Network
DNS
Server
Web
Server
Sensor
Sensor
Firewall
Sensor
Router
Untrusted Network

## Slide 18: Cisco IPS Solutions AIM and Network Module Enhanced
Integrates IPS into the Cisco 1841 (IPS AIM only), 2800 and 3800 ISR routers
IPS AIM occupies an internal AIM slot on router and has its own CPU and DRAM
Monitors up to 45 Mb/s of traffic
Provides full-featured intrusion protection
Is able to monitor traffic from all router interfaces
Can inspect GRE and IPsec traffic that has been decrypted at the router
Delivers comprehensive intrusion protection at branch offices, isolating threats from the corporate network
Runs the same software image as Cisco IPS Sensor Appliances

## Slide 19: Cisco IPS Solutions ASA AIP-SSM
High-performance module designed to provide additional security services to the Cisco ASA 5500 Series Adaptive Security Appliance
Diskless design for improved reliability
External 10/100/1000 Ethernet interface for management and software downloads
Intrusion prevention capability
Runs the same software image as the Cisco IPS Sensor appliances

## Slide 20: Cisco IPS Solutions 4200 Series Sensors
Appliance solution focused on protecting network devices, services, and applications
Sophisticated attack detection is provided.

## Slide 21: Cisco IPS Solutions Cisco Catalyst 6500 Series IDSM-2
Switch-integrated intrusion protection module delivering a high-value security service in the core network fabric device
Support for an unlimited number of VLANs
Intrusion prevention capability
Runs the same software image as the Cisco IPS Sensor Appliances

## Slide 22: IPS Sensors
Factors that impact IPS sensor selection and deployment:
  Amount of network traffic
  Network topology
  Security budget
  Available security staff
Size of implementation
  Small (branch offices)
  Large
  Enterprise

## Slide 23: Comparing HIPS and Network IPS
 | Advantages | Disadvantages
HIPS | Is host-specific Protects host after decryption Provides application-level encryption protection | Operating system dependent Lower level network events not seen Host is visible to attackers
Network IPS | Is cost-effective Not visible on the network Operating system independent Lower level network events seen | Cannot examine encrypted traffic Does not know whether an attack was successful

## Slide 24: Signature Characteristics
Hey, come look at this. This looks like the signature of a LAND attack.
An IDS or IPS sensor matches a signature with a data flow
The sensor takes action
Signatures have three distinctive attributes
  Signature type
  Signature trigger
  Signature action

## Slide 25: Signature Types
Atomic
  Simplest form
  Consists of a single packet, activity, or event
  Does not require intrusion system to maintain state information
  Easy to identify
Composite
  Also called a stateful signature
  Identifies a sequence of operations distributed across multiple hosts
  Signature must maintain a state known as the event horizon

## Slide 26: Signature File

## Slide 27: Signature Micro-Engines
Version 4.x SME Prior 12.4(11)T | Version 5.x SME 12.4(11)T and later | Description
ATOMIC.IP | ATOMIC.IP | Provides simple Layer 3 IP alarms
ATOMIC.ICMP | ATOMIC.IP | Provides simple Internet Control Message Protocol (ICMP) alarms based on the following parameters: type, code, sequence, and ID
ATOMIC.IPOPTIONS | ATOMIC.IP | Provides simple alarms based on the decoding of Layer 3 options
ATOMIC.UDP | ATOMIC.IP | Provides simple User Datagram Protocol (UDP) packet alarms based on the following parameters: port, direction, and data length
ATOMIC.TCP | ATOMIC.IP | Provides simple TCP packet alarms based on the following parameters: port, destination, and flags
SERVICE.DNS | SERVICE.DNS | Analyzes the Domain Name System (DNS) service
SERVICE.RPC | SERVICE.RPC | Analyzes the remote-procedure call (RPC) service
SERVICE.SMTP | STATE | Inspects Simple Mail Transfer Protocol (SMTP)
SERVICE.HTTP | SERVICE.HTTP | Provides HTTP protocol decode-based string engine that includes ant evasive URL de-obfuscation
SERVICE.FTP | SERVICE.FTP | Provides FTP service special decode alarms
STRING.TCP | STRING.TCP | Offers TCP regular expression-based pattern inspection engine services
STRING.UDP | STRING.UDP | Offers UDP regular expression-based pattern inspection engine services
STRING.ICMP | STRING.ICMP | Provides ICMP regular expression-based pattern inspection engine services
MULTI-STRING | MULTI-STRING | Supports flexible pattern matching and supports Trend Labs signatures
OTHER | NORMALIZER | Provides internal engine to handle miscellaneous signatures
Atomic – Examine simple packets
Service – Examine the many services that are attacked
String – Use expression-based patterns to detect intrusions
Multi-String Supports flexible pattern matching
Other – Handles miscellaneous signatures

## Slide 28: Cisco Signature List

## Slide 29: Signature Triggers
 | Advantages | Disadvantages
Pattern-based Detection | Easy configuration Fewer false positives Good signature design | No detection of unknown signatures Initially a lot of false positives Signatures must be created, updated, and tuned
Anomaly-based Detection | Simple and reliable Customized policies Can detect unknown attacks | Generic output Policy must be created
Policy-based Detection | Easy configuration Can detect unknown attacks | Difficult to profile typical activity in large networks Traffic profile must be constant
Honey Pot-Based Detection | Window to view attacks Distract and confuse attackers Slow down and avert attacks Collect information about attack | Dedicated honey pot server Honey pot server must not be trusted

## Slide 30: Pattern-based Detection
Trigger | Signature Type | 
 | Atomic Signature | Stateful Signature
Pattern-based detection | No state required to examine pattern to determine if signature action should be applied | Must maintain state or examine multiple items to determine if signature action should be applied
Example | Detecting for an Address Resolution Protocol (ARP) request that has a source Ethernet address of FF:FF:FF:FF:FF:FF | Searching for the string confidential across multiple packets in a TCP session

## Slide 31: Anomaly-based Detection
Trigger | Signature Type | 
 | Atomic Signature | Stateful Signature
Anomaly-based detection | No state required to identify activity that deviates from normal profile | State required to identify activity that deviates from normal profile
Example | Detecting traffic that is going to a destination port that is not in the normal profile | Verifying protocol compliance for HTTP traffic

## Slide 32: Policy-based Detection
Signature Trigger | Signature Type | 
 | Atomic Signature | Stateful Signature
Policy-based detection | No state required to identify undesirable behavior | Previous activity (state) required to identify undesirable behavior
Example | Detecting abnormally large fragmented packets by examining only the last fragment | A SUN Unix host sending RPC requests to remote hosts without initially consulting the SUN PortMapper program.

## Slide 33: Honey Pot-based Detection
Uses a dummy server to attract attacks
Distracts attacks away from real network devices
Provides a means to analyze incoming types of attacks and malicious traffic patterns
Is useful for finding common attacks on network resources and implementing patches/fixes for real network purposes

## Slide 34: Cisco IOS IPS Solution Benefits
Uses the underlying routing infrastructure to provide an additional layer of security with investment protection
Attacks can be effectively mitigated to deny malicious traffic from both inside and outside the network
Provides threat protection at all entry points to the network when combined with other Cisco solutions
Is supported by easy and effective management tools
Offers pervasive intrusion prevention solutions that are designed to integrate smoothly into the network infrastructure and to proactively protect vital resources
Supports approximately 2000 attack signatures from the same signature database that is available for Cisco IPS appliances

## Slide 35: Signature Alarms
Alarm Type | Network Activity | IPS Activity | Outcome
False positive | Normal user traffic | Alarm generated | Tune alarm
False negative | Attack traffic | No alarm generated | Tune alarm
True positive | Attack traffic | Alarm generated | Ideal setting
True negative | Normal user traffic | No alarm generated | Ideal setting

## Slide 36: Signature Tuning Levels
Low – Abnormal network activity is detected, could be malicious, and immediate threat is not likely
Medium - Abnormal network activity is detected, could be malicious, and immediate threat is likely
High – Attacks used to gain access or cause a DoS
attack are detected (immediate threat extremely likely
Informational – Activity that triggers the signature is not an immediate threat, but the information provided is useful

## Slide 37: Generating an Alert
Specific Alert | Description
Produce alert | This action writes the event to the Event Store as an alert.
Produce verbose alert | This action includes an encoded dump of the offending packet in the alert.

## Slide 38: Logging the Activity
Specific Alert | Description
Log attacker packets | This action starts IP logging on packets that contain the attacker address and sends an alert.
Log pair packets | This action starts IP logging on packets that contain the attacker and victim address pair.
Log victim packets | This action starts IP logging on packets that contain the victim address and sends an alert.

## Slide 39: Dropping/Preventing the Activity
Specific Alert | Description
Deny attacker inline | Terminates the current packet and future packets from this attacker address for a period of time. The sensor maintains a list of the attackers currently being denied by the system. Entries may be removed from the list manually or wait for the timer to expire. The timer is a sliding timer for each entry. If the denied attacker list is at capacity and cannot add a new entry, the packet is still denied.
Deny connection inline | Terminates the current packet and future packets on this TCP flow.
Deny packet inline | Terminates the packet.

## Slide 40: Resetting a TCP Connection/Blocking Activity/Allowing Activity
Category | Specific Alert | Description
Resetting a TCP connection | Reset TCP connection | Sends TCP resets to hijack and terminate the TCP flow
Blocking future activity | Request block connection | This action sends a request to a blocking device to block this connection.
 | Request block host | This action sends a request to a blocking device to block this attacker host.
 | Request SNMP trap | Sends a request to the notification application component of the sensor to perform SNMP notification.
Allowing Activity |  | Allows administrator to define exceptions to configured signatures

## Slide 41: Planning a Monitoring Strategy
The MARS appliance detected and mitigated the ARP poisoning attack.
There are four factors to consider when planning a monitoring strategy.
  Management method
  Event correlation
  Security staff
  Incident response plan

## Slide 42: MARS
The security operator examines the output generated by the MARS appliance:
  MARS is used to centrally manage all IPS sensors.
  MARS is used to correlate all of the IPS and Syslog events in a central location.
  The security operator must proceed according to the incident response plan identified in the Network Security Policy.

## Slide 43: Cisco IPS Solutions
Locally Managed Solutions:
  Cisco Router and Security Device Manager (SDM)
  Cisco IPS Device Manager (IDM)
Centrally Managed Solutions:
  Cisco IDS Event Viewer (IEV)
  Cisco Security Manager (CSM)
  Cisco Security Monitoring, Analysis, and Response System (MARS)

## Slide 44: Cisco Router and Security Device Manager
Lets administrators control the application of Cisco IOS IPS on interfaces, import and edit signature definition files (SDF) from Cisco.com, and configure the action that Cisco IOS IPS is to take if a threat is detected
Monitors and prevents intrusions by comparing traffic against signatures of known threats and blocking the traffic when a threat is detected

## Slide 45: Cisco IPS Device Manager
A web-based configuration tool
Shipped at no additional cost with the Cisco IPS Sensor Software
Enables an administrator to configure and manage a sensor
The web server resides on the sensor and can be accessed through a web browser

## Slide 46: Cisco IPS Event Viewer
View and manage alarms for up to five sensors
Connect to and view alarms in real time or in imported log files
Configure filters and views to help you manage the alarms.
Import and export event data for further analysis.

## Slide 47: Cisco Security Manager
Powerful, easy-to-use solution to centrally provision all aspects of device configurations and security policies for Cisco firewalls, VPNs, and IPS
Support for IPS sensors and Cisco IOS IPS
Automatic policy-based IPS sensor software and signature updates
Signature update wizard

## Slide 48: Cisco Security Monitoring Analytic and Response System
An appliance-based, all-inclusive solution that allows network and security administrators to monitor, identify, isolate, and counter security threats
Enables organizations to more effectively use their network and security resources.
Works in conjunction with Cisco CSM.

## Slide 49: Secure Device Event Exchange
The SDEE format was developed to improve communication of events generated by security devices
Allows additional event types to be included as they are defined
Network Management Console
Alarm
SDEE Protocol
Syslog Server
Alarm
Syslog

## Slide 50: Best Practices
The need to upgrade sensors with the latest signature packs must be balanced against the momentary downtime.
When setting up a large deployment of sensors, automatically update signature packs rather than manually upgrading every sensor.
When new signature packs are available, download the new signature packs to a secure server within the management network. Use another IPS to protect this server from attack by an outside party.
Place the signature packs on a dedicated FTP server within the management network. If a signature update is not available, a custom signature can be created to detect and mitigate a specific attack.

## Slide 51: Best Practices
Configure the FTP server to allow read-only access to the files within the directory on which the signature packs are placed only from the account that the sensors will use.
Configure the sensors to automatically update the signatures by checking the FTP server for the new signature packs periodically. Stagger the time of day when the sensors check the FTP server for new signature packs.
The signature levels that are supported on the management console must remain synchronized with the signature packs on the sensors themselves.

## Slide 52: Overview of Implementing IOS IPS
Download the IOS IPS files
Create an IOS IPS configuration directory on Flash
Configure an IOS IPS crytpo key
Enable IOS IPS
Load the IOS IPS Signature Package to the router
I want to use CLI to manage my signature files for IPS. I have downloaded the IOS IPS files.

## Slide 53: 1. Download the Signature File
Download IOS IPS signature package files and public crypto key

## Slide 54: 2. Create Directory
R1# mkdir ips
Create directory filename [ips]?
Created dir flash:ips
R1#
R1# dir flash:
Directory of flash:/
5 -rw- 51054864 Jan 10 2009 15:46:14 -08:00
c2800nm-advipservicesk9-mz.124-20.T1.bin
6 drw- 0 Jan 15 2009 11:36:36 -08:00 ips
64016384 bytes total (12693504 bytes free)
R1#
R1# rename ips ips_new
Destination filename [ips_new]?
R1#
To rename a directory:

## Slide 55: 3. Configure the Crypto Key
R1# conf t
R1(config)#
1
2
1 – Highlight and copy the text contained in the public key file.
2 – Paste it in global configuration mode.

## Slide 56: Confirm the Crypto Key
R1# show run
<Output omitted>
crypto key pubkey-chain rsa
named-key realm-cisco.pub signature
key-string
30820122 300D0609 2A864886 F70D0101 01050003 82010F00 3082010A 02820101
00C19E93 A8AF124A D6CC7A24 5097A975 206BE3A2 06FBA13F 6F12CB5B 4E441F16
17E630D5 C02AC252 912BE27F 37FDD9C8 11FC7AF7 DCDD81D9 43CDABC3 6007D128
B199ABCB D34ED0F9 085FADC1 359C189E F30AF10A C0EFB624 7E0764BF 3E53053E
5B2146A9 D7A5EDE3 0298AF03 DED7A5B8 9479039D 20F30663 9AC64B93 C0112A35
FE3F0C87 89BCB7BB 994AE74C FA9E481D F65875D6 85EAF974 6D9CC8E3 F0B08B85
50437722 FFBE85B9 5E4189FF CC189CB9 69C46F9C A84DFBA5 7A0AF99E AD768C36
006CF498 079F88F8 A3B3FB1F 9FB7B3CB 5539E1D1 9693CCBB 551F78D2 892356AE
2F56D826 8918EF3C 80CA4F4D 87BFCA3B BFF668E9 689782A5 CF31CB6E B4B094D3
F3020301 0001
<Output omitted>

## Slide 57: 4. Enable IOS IPS
R1(config)# ip ips name iosips
R1(config)# ip ips name ips list ?
<1-199> Numbered access list
WORD Named access list
R1(config)#
R1(config)# ip ips config location flash:ips
R1(config)#
2 – IPS location in flash identified
1
2
R1(config)# ip http server
R1(config)# ip ips notify sdee
R1(config)# ip ips notify log
R1(config)#
3 – SDEE and Syslog notification are enabled
3
1 – IPS rule is created

## Slide 58: 4. Enable IOS IPS
R1(config)# ip ips signature-category
R1(config-ips-category)# category all
R1(config-ips-category-action)# retired true
R1(config-ips-category-action)# exit
R1(config-ips-category)#
R1(config-ips-category)# category ios_ips basic
R1(config-ips-category-action)# retired false
R1(config-ips-category-action)# exit
R1(config-ips-category)# exit
Do you want to accept these changes? [confirm] y
R1(config)#
2 – The IPS basic category is unretired.
1
2
R1(config)# interface GigabitEthernet 0/1
R1(config-if)# ip ips iosips in
R1(config-if)# exit
R1(config)#exit
R1(config)# interface GigabitEthernet 0/1
R1(config-if)# ip ips iosips in
R1(config-if)# ip ips iosips out
R1(config-if)# exit
R1(config)# exit
4 – The IPS rule is applied in an incoming and outgoing direction.
3
4
1 – The IPS all category is retired
3 – The IPS rule is applied in a incoming direction

## Slide 59: 5. Load Signature Package
R1# copy ftp://cisco:cisco@10.1.1.1/IOS-S376-CLI.pkg idconf
Loading IOS-S310-CLI.pkg !!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
[OK - 7608873/4096 bytes]
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_BUILDS_STARTED: 16:44:47 PST Jan 15 2008
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_BUILDING: multi-string - 8 signatures - 1 of 13 engines
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_READY: multi-string - build time 4 ms - packets for this
engine will be scanned
*Jan 15 16:44:47 PST: %IPS-6-ENGINE_BUILDING: service-http - 622 signatures - 2 of 13 engines
*Jan 15 16:44:53 PST: %IPS-6-ENGINE_READY: service-http - build time 6024 ms - packets for this
engine will be scanned
<Output omitted>
*Jan 15 16:45:18 PST: %IPS-6-ENGINE_BUILDING: service-smb-advanced - 35 signatures - 12 of 13 engines
*Jan 15 16:45:18 PST: %IPS-6-ENGINE_READY: service-smb-advanced - build time 16 ms - packets
for this engine will be scanned
*Jan 15 16:45:18 PST: %IPS-6-ENGINE_BUILDING: service-msrpc - 25 signatures - 13 of 13 engines
*Jan 15 16:45:18 PST: %IPS-6-ENGINE_READY: service-msrpc - build time 32 ms - packets for this
engine will be scanned
*Jan 15 16:45:18 PST: %IPS-6-ALL_ENGINE_BUILDS_COMPLETE: elapsed time 31628 ms
2 – Signature compiling begins immediately after the signature package is loaded to the router.
1
2
1 – Copy the signatures from the FTP server.

## Slide 60: Verify the Signature
R1# show ip ips signature count
Cisco SDF release version S310.0 ← signature package release version
Trend SDF release version V0.0
Signature Micro-Engine: multi-string: Total Signatures 8
multi-string enabled signatures: 8
multi-string retired signatures: 8
<Output omitted>
Signature Micro-Engine: service-msrpc: Total Signatures 25
service-msrpc enabled signatures: 25
service-msrpc retired signatures: 18
service-msrpc compiled signatures: 1
service-msrpc inactive signatures - invalid params: 6
Total Signatures: 2136
Total Enabled Signatures: 807
Total Retired Signatures: 1779
Total Compiled Signatures:
351 ← total compiled signatures for the IOS IPS Basic category
Total Signatures with invalid parameters: 6
Total Obsoleted Signatures: 11
R1#

## Slide 61: Configuring Cisco IOS IPS in SDM
Create IPS – this tab contains the IPS Rule wizard
Edit IPS – this tab allows the edit of rules and apply or remove them from interfaces
Security Dashboard– this tab is used to view the Top Threats table and deploy signatures
IPS Migration – this tab is used to migrate configurations created in earlier versions of the IOS

## Slide 62: Using SDM
1. Choose Configure > Intrusion Prevention > Create IPS
2. Click the Launch IPS Rule Wizard button
3. Click Next

## Slide 63: Using SDM
4. Choose the router interface by checking either the Inbound or Outbound checkbox (or both)
5. Click Next

## Slide 64: Using SDM
6. Click the preferred option and fill in the appropriate text box
7. Click download for the latest signature file
8. Go to www.cisco.com/pcgi-bin/tablebuild.pl/ios-v5sigup to obtain the public key
9. Download the key to a PC
10. Open the key in a text editor and copy the text after the phrase “named-key” into the Name field
11. Copy the text between the phrase “key-string” and the work “quit” into the Key field
12. Click Next

## Slide 65: Using SDM
13. Click the ellipsis (…) button and enter config location
14. Choose the category that will allow the Cisco IOS IPS to function efficiently on the router
15. Click finish

## Slide 66: SDM IPS Wizard Summary

## Slide 67: Generated CLI Commands
R1# show run
<Output omitted>
ip ips name sdm_ips_rule
ip ips config location flash:/ipsdir/ retries 1
ip ips notify SDEE
!
ip ips signature-category
category all
retired true
category ios_ips basic
retired false
!
interface Serial0/0/0
ip ips sdm_ips_rule in
ip virtual-reassembly
<Output omitted>

## Slide 68: Using CLI Commands
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# ip ips signature-definition
R1(config-sigdef)# signature 6130 10
R1(config-sigdef-sig)# status
R1(config-sigdef-sig-status)# retired true
R1(config-sigdef-sig-status)# exit
R1(config-sigdef-sig)# exit
R1(config-sigdef)# exit
Do you want to accept these changes? [confirm] y
R1(config)#
This example shows how to retire individual signatures. In this case, signature 6130 with subsig ID of 10.
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# ip ips signature-category
R1(config-ips-category)# category ios_ips basic
R1(config-ips-category-action)# retired false
R1(config-ips-category-action)# exit
R1(config-ips-category)# exit
Do you want to accept these changes? [confirm] y
R1(config)#
This example shows how to unretire all signatures that belong to the IOS IPS Basic category.

## Slide 69: Using CLI Commands for Changes
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# ip ips signature-definition
R1(config-sigdef)# signature 6130 10
R1(config-sigdef-sig)# engine
R1(config-sigdef-sig-engine)# event-action produce-alert
R1(config-sigdef-sig-engine)# event-action deny-packet-inline
R1(config-sigdef-sig-engine)# event-action reset-tcp-connection
R1(config-sigdef-sig-engine)# exit
R1(config-sigdef-sig)# exit
R1(config-sigdef)# exit
Do you want to accept these changes? [confirm] y
R1(config)#
This example shows how to change signature actions to alert, drop, and reset for signature 6130 with subsig ID of 10.

## Slide 70: Viewing Configured Signatures
Choose Configure > Intrusion Prevention > Edit IPS > Signatures > All Categories
Filter the signature list according to type
To modify a signature, right-click on the signature then choose an option from the pop-up

## Slide 71: Modifying Signature Actions
To tune a signature, choose Configure > Intrusion Prevention > Edit IPS > Signatures > All Categories
To modify a signature action, right-click on the signature and choose Actions
Notes: Deny Attacker Inline: Create an ACL that denies all traffic from the IP address that is considered the source of the attack by the Cisco IOS IPS system.
Deny Connection Inline: Drop the packet and all future packets from this TCP flow.
Deny Packet Inline: Do not transmit this packet (inline only).
Produce Alert: Generate an alarm message.
Reset TCP Connection: Send TCP resets to terminate the TCP flow.

## Slide 72: Editing Signature Parameters
Choose the signature and click Edit
Different signatures have different parameters that can be modified:
Signature ID
Sub Signature ID
Alert Severity
Sig Description
Engine
Event Counter
Alert Frequency
Status

## Slide 73: Using CLI Commands
The show ip ips privileged EXEC command can be used with several other parameters to provide specific IPS information.
The show ip ips all command displays all IPS configuration data.
The show ip ips configuration command displays additional configuration data that is not displayed with the show running-config command.
The show ip ips interface command displays interface configuration data. The output from this command shows inbound and outbound rules applied to specific interfaces.

## Slide 74: Using CLI Commands
The show ip ips signature verifies the signature configuration. The command can also be used with the key word detail to provide more explicit output
The show ip ips statistics command displays the number of packets audited and the number of alarms sent. The optional reset keyword resets output to reflect the latest statistics.
Use the clear ip ips configuration command to remove all IPS configuration entries, and release dynamic resources. The clear ip ips statistics command resets statistics on packets analyzed and alarms sent.

## Slide 75: Using SDM
Choose Configure > Intrusion Prevention > Edit IPS
All of the interfaces on the router display showing if they are enabled or disabled

## Slide 76: Reporting IPS Intrusion Alerts
To specify the method of event notification, use the ip ips notify [log | sdee] global configuration command.
  The log keyword sends messages in syslog format.
  The sdee keyword sends messages in SDEE format.
R1# config t
R1(config)# logging 192.168.10.100 R1(config)# ip ips notify log
R1(config)# logging on
R1(config)#
Notes: This graphic needs some explanatory text.

## Slide 77: SDEE on an IOS IPS Router
Enable SDEE on an IOS IPS router using the following command:
Enable HTTP or HTTPS on the router
SDEE uses a pull mechanism
Additional commands:
  ip sdee events events
  Clear ip ips sdee {events|subscription}
  ip ips notify
R1# config t R1(config)# ip http server
R1(config)# ip http secure-server
R1(config)# ips notify sdee
R1(config)# ip sdee events 500
R1(config)#

## Slide 78: Using SDM to View Messages
To view SDEE alarm messages, choose Monitor > Logging > SDEE Message Log
To view Syslog messages, choose Monitor > Logging > Syslog